## Slide 1: Short-Time Spectral Attenuator and process inversion for Musical Effect
Alessandri Roberto
Cicognani Roberto Leone

## Slide 2
Content
Introduction
Methodology
Objectives
Results and Discussion
Conclusion
Further Recommendations

## Slide 3
High Quality Audio Today
Nostalgia and Necessity
Random Background Noise
Perceived as “hiss”
Electrical and Environmental Origin
Noise at all frequencies
Introduction: Context

## Slide 4
Why STSA?
Not stationary signals and little knowledge needed
Non-distruptive analysis in freq domain
Speech Enhancement and Recording Restoration
Music Effect by Inversion
Song Resynthesis
Introduction: Problem Formulation

## Slide 5
s[n]
v[n]
x[n]
y[n]
Restoration
Methodology: Model of Noise
Additive, uncorrelated, stationary
s[n]: signal without noise
v[n]: noise
x[n]: our signal !
y[n]: output
Sx: power spectrum of clean
Sn: power spectrum of noise

## Slide 6
Methodology: STSA
x[n]
Short-Time Analysis
Spectral Gain
Short-Time Synthesis
y[n]
Noise Power Level Estimate
Noise Suppression Rule
Suppression Rules:
Power Spectral Matching
Wiener Filter
Spectral Matching

## Slide 7
Methodology: the Music Effect
What if instead of attenuating the noise we enhance it?
Add special noise to clean sound as a musical effect
Using the inverse of the suppression rules

## Slide 8
Methodology: STSE
x[n]
Short-Time Analysis
Spectral Gain
y[n]
Noise Power Level Estimate
Noise Suppression Rule
Short-Time Sinusoidal Re-Synthesis
Function Inversion

## Slide 9
Methodology: Short-Time Processing Parameters
Choice of the length of the window
Longer: Level of signal components cancelled increases with the bandwidth (40 ms)
Shorter: Pure tone and noise correlation issues (20-30 ms)
Choice of hopsize: avoid aliasing(50-75%)
N = 1024 or 2048

## Slide 10
Short-time Analysis
Locate Noisiest frame
Power Spectrum Density Extimation
ZCR and STE Calculation
Methodology: Noise Estimation

## Slide 11
Methodology: Noise Power Spectrum Estimate

## Slide 12
Signal Segmentation and FFT
Gain Estimation
Signal Filtering and IFFT
Reconstruct the Signal
Methodology: Suppression Rule Application

## Slide 13
Signal Segmentation and FFT
Gain Estimation
Gain Inversion
Signal Filtering and IFFT
Reconstruct the Signal
Methodology: Enhancement Rule Application

## Slide 14
Sinusoidal Oscillator
Spectrum Resynthesizer
Frame-by-Frame Spectrum Resynthesis
Methodology: Sinusoidal Oscillator

## Slide 15
STSA Implementation “by the book”
Suppression rules comparison
Process Inversion
Check quality of Sinusoidal Resynthesis
Objectives of the project
Notes: .

## Slide 16
Results
Noisy Record
Clean Record

## Slide 17
Difficult to analyze the results of STSA generally
STSA doesn’t reduce the noise present in sub-bands with signal components
Easier with a pure tone than a a wideband signal
Results: Limitations

## Slide 18
Remaining noise’s quality
Short-lived tones with randomly distributed frequencies
“Birdsong”
Results: Musical Noise

## Slide 19
Results
Noisy Record
Clean Record

## Slide 20
Signals after the process have a clearly audible noise
Signals results to be also quite distorted
Frame-by-Frame Spectrum Resynthesis is Computationally Demanding
Results

## Slide 21
Better localize the frame that seems to have “uncorrelated Gaussian noise”
Make the algorithm Suppression-rule Adaptive (SNR?)
Try different Enhancement Rules instead of inverting Suppression ones
Try different types of synthesis
Conclusions and Further Recommendations

## Slide 22: THANK YOU FOR YOUR ATTENTION!